## Slide 1
Please remember to be considerate of our instructors and your fellow students and silence your Cell Phones and Pagers before class starts.

## Slide 2
“Equipment For Your Boat”

## Slide 3: LAWS and RULES
Federal rules
State rules
Links to these are on our website
Notes: You should be familiar and know what the differences are between Federal Rules and State Rules.

## Slide 4
Page 47. Negligent Operation
Federal law prohibits the negligent or grossly negligent operation of a vessel and / or interference with the safe operation of a vessel, so as to endanger lives and / or property. The U.S. Coast Guard may impose a civil penalty for negligent operation. Grossly negligent operation is a criminal offense and an operator may be fined up $5,000.00, imprisoned for one year, or both.

## Slide 5: Some examples of actions that may constitute negligent or grossly negligent operations:
Operating a boat while under the influence of alcohol or drugs.
Operating a boat in a swimming area.
Excessive speed in the vicinity of other boats or in dangerous waters.
Hazardous water-
skiing practices.
Bow-riding, also seatback, gunwale, or transom riding.

## Slide 6: Power Driven Vessels
Definition for Power Driven Vessel:
Any vessel propelled by machinery (motor).
Sometimes people forget that a sailboat with an engine becomes a power boat when the engine is running.
Must Be:
State Registered or Documented by U.S. Coast Guard.
Notes: Even though Documented still must pay State Excise tax and display state validation sticker.

## Slide 7
For link refer to Instructor's Reference Page
Notes: URL: Links in our PowerPoints can be found on our Flotilla Websites Schedule page. There is also a QR Code to the URL links page.

## Slide 8: DOCUMENTATION
Advantages:
May fly the “yacht ensign”
Boat’s papers, e.g., title and bill of sale Recorded with Federal authorities.
Original documentation papers must be onboard.
Gives preferred status for mortgages.
Requirements:
Owner/Captain must be US citizen.
Documented boats over 5 net tons or 27’.
Lasts 1 to 5 years

## Slide 9: DOCUMENTATION NUMBER
Must start with "NO." Numbers in block-type Arabic numerals at least three inches high on some clearly visible interior structural part of the hull. Number must be permanently affixed to prevent removal.

## Slide 10: DOCUMENTED BOAT
Name, hailing port and State on exterior part of the hull.
Must be 4” > heigh, in clear Latin or Arabic letters, and Roman or Arabic numerals.

## Slide 11: DOCUMENTATION REQUIREMENTS
States differ in requirements for a documented boats.
Maine requires a documented boat to pay state excise tax and display a valid registration sticker, but you don’t have to register the boat.
If you move, a registered boat must be register in new state within 60 days.
Notes: State of Maine all vessels propelled by machinery must be registered or documented.
Maine requires a documented boat to pay state excise tax and display a valid registration sticker, but you don’t have to register the boat.

## Slide 12: REGISTERATION REQUIREMENTS
States differ in requirements for registration of dinghies, and non-powered boats.
Federal Law: Dinghies or Service vessel to a documented boat only need to indicate the dinghy or service vessel identify to the boat they service.
State of Maine does not recognize this and requires dinghies or service vessels be registered for vessels documented with a Maine State port documentation.
Register in State where mainly used.
Notes: Federal Law allows for Dinghies or Service vessel to a documented boat only need to indicate the dinghy or service vessel identify to boat they service. State of Maine does not recognize this and requires service vessels and dinghies be registered with the state.

## Slide 13: STATE REGISTRATION COST for 2025
Motorboats
(0-10hp) - $16.00 Saltwater ($26.00 with Milfoil)
(11hp-50hp) - $21.00 Saltwater ($31.00) with Milfoil
(51hp-115hp) - $27.00 ($37.00 with Milfoil)
(115hp >) - $37.00 ($45.00 with Milfoil)
Personal Watercraft- $35.00 ($45.00 with Milfoil)
Original certificate must always be on-board (ME)
New registrations must be done in person.
Reregistration can be done online at Department of Inland Fisheries and Wildlife.
There is a $4.50 agent fee for registering online.
Additionally, you will have to pay State Excise Tax.
Notes: SECTION VIII. VESSEL REGISTRATION NUMBER
A. The number issued pursuant to these regulations shall be in accordance with the pattern described in this subsection.
1. The vessel registration number shall be divided into three parts, for the purpose of providing a combination of numerals and letters which furnish individual vessel registration numbers.
2. The first part of the number shall be an abbreviation in capital letters of the State of Maine – ME –and shall be followed by a space equal to the letter H.
3. The second part of the number shall be a group of digits consisting of four Arabic numerals appearing after the letters ME, and shall be followed by a space equal to the letter H.
4. The remainder of the number shall consist of no more than two capital letters, in sequence, in accordance with the serials numerically and alphabetically.
5. Validation stickers should be within 4” of the last suffix letter. Directions on the back of the validation sticker are correct. However, the images are not and should not be use on how to apply the stickers.
6. Since the letters “I”, “O”, and “Q” may be mistaken for Arabic Numerals, all letters' sequences using “I”, “O”, and “Q” shall be omitted. Objectionable words formed by the use of letters will not be used.

## Slide 14
STATE REGISTRATION NUMBER
ME 17 HRR
Number on the registration certificate must be placed on vessel.
Notes: Should make sure that Serial Number and Hull Identification Number match. Especially on older boats. Note that Registration Number does not have the ME before it and the suffix letter doesn’t show a space between them and the number. Re-registrations can be done online on the State of Maine’s website, and you get an immediate temporary registration that is good until you get you validation sticker and registration. New registration must be made in person at your town’s office.

## Slide 15
Back of Registration Stickers
Correct
Notes: On the back of your validation sticker, it tell you how and where to place your registration numbers and the validation sticker. The wording is correct. However, the image for the Starboard side of the boat is wrong. In Maine, the validation sticker always goes within 4” of the last letter of the registration regardless of which side of the boat it is on.

## Slide 16
STATE REGISTRATION NUMBER
Numbers clearly visible bow side or forward half of boat.
In a contrasting color to hull.
Block letters at least 3” high
Ooops!

## Slide 17: STATE REGISTRATION
  May be good for one or several years, differs by State.
  ME starts Jan 1st, renew early.
  Place decal on boat where required by your state.
  Numbers stay with the boat if you sell within the state.
  Report to issuing state authority if vessel is lost or stolen or registration is lost.
Notes: State of Maine one year January 1 through December 31.
State of Maine can be renewed any time before boat goes into the water for that year.

## Slide 18
Only inflatables can hang registration #s on a plate.
All other boat must be permanently affixed to forward half of the vessel.
INFLATABLE BOAT NUMBERING
Notes: The only time a registration numbers are allowed to be put on a hanging placard is on an inflatable boat. All other boat registration number must shall be painted on, or attached to, each side of the forward half of the vessel

## Slide 19
State ID missing, spacing.
Notes: Spacing – state ID ME missing

## Slide 20
Only Dealers can display registration this way.
Must be permanently affixed to forward half of the vessel
Notes: Not permanently affixed

## Slide 21
Maine ingenuity at it best.
Notes: Maine ingenuity at it best. Must be on the outside of the hull

## Slide 22
A temporary registration awaiting numbers?
Notes: Could be a temporary registration awaiting numbers

## Slide 23
Could be a good registration if it is a tender to a Documented boat not from the State of Maine
Notes: Possibly could be a good registration if it is a tender to a Documented boat not from the State of Maine

## Slide 24
TT ME 3679 T stands for Tender Too ME 3679T; not allowed in Maine.
This dinghy should be a registered boat in Maine.
Notes: TT ME 3679 T stands for Tender Too ME 3679 T Not allowed in Maine. This dinghy should be a registered boat in Maine.

## Slide 25
State Validation Sticker are not Trophies
Only current year displayed.
Spacing wrong – one numeral is not contrasting to hull color.
Notes: State Validation Sticker are not Trophies
Only current year should be displayed plus
Spacing wrong – one numeral is not contrasting to hull

## Slide 26: HULL IDENTIFICATION NUMBER - HIN
HIN appears on starboard side of transom within two inches of top.
If placement can’t be on transom, it is on the starboard side, two inches from top of hull and within one foot of transom.
On pontoon boats HIN is on the aft crossbeam within one foot of starboard hull attachment.

## Slide 27: HULL IDENTIFICATION NUMBER - HIN
Boats built between November 1, 1972 and July 31, 1984 have HIN number which looks like:

## Slide 28: HULL IDENTIFICATION NUMBER - HIN
Boats built after August 1984 have a number as shown:

## Slide 29: LENGTH OF BOAT
Official boat length is measured along a straight line parallel to its keel.
Important as it may put you in a high class with more requirements

## Slide 30: Classification of Boats
Class A: Less than 16’ in length.
Class 1: 16’ to less than 26’ in length
Class 2: 26’ to less than 40’ in length
Class 3: 40’ to less than 65’ in length
Be aware some boat manufacturers use metric units; a rounded-up conversion may not be to your advantage – check calculations.

## Slide 31: CAPACITY PLATE
Required on monohull boats less than 20 feet long.
Sailboats, canoes, kayaks & inflatable boats are exempt but may have this.
Usually combined with compliance plate.

## Slide 32: CAPACITY PLATE
Max permitted hp of outboard engines.
Max weight of people on board.
Max weight total of people & equipment (including engine).
Notes: Overloading and Overpowering.
No vessel may be loaded with passengers or cargo beyond its safe cargo carrying capacity.
The maximum persons capacity marked on a vessel's maximum capacities plate must not be exceeded.
The maximum weight capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe loading requirements.
Overpowering
No vessel may be operated beyond its safe powering capacity.
The maximum horsepower capacity marked on a vessel's maximum capacities plate must not be exceeded.
If a vessel does not have a U.S. Coast Guard maximum Capacities plate provided by the manufacturer, the owner must demonstrate that his or her vessel conforms to the U. S. Coast Guard safe powering requirements.

## Slide 33: CAPACITY PLATE - Safety
Capacities given for normal conditions.
Overloaded for specific current conditions.
Must be visible to helm when getting underway.
All capacities must be obeyed.

## Slide 34: MANUFACTURER’S CERTIFICATE OF COMPLIANCE
May be combined with capacity plate
Required on motorboats less than 20 ft long
“This boat complies with U S Coast Guard standards in effect on the date of certification”

## Slide 35: Ventilation Requirements
Best detector – Your NOSE!
Exhaust fumes can cause carbon monoxide poisoning – detectors are available
Many fires/explosions caused by gasoline fumes in enclosed engine/fuel compartments

## Slide 36: Natural Ventilation System
Natural system - air circulates through closed spaces due to motion of boat.
Intake, higher!
Exhaust, lower!

## Slide 37: Powered Ventilation System
Powered system - air circulates because of motor driven fans.
Need to be checked as the hoses can shake loose.
Exhaust opening located just above the usual water level in the bilge.

## Slide 38: WARNING
  Gas vapors can easily explode.
  Before starting engine, operate blower for four minutes and check engine compartment bilge for gas vapors.
  Sniff to be sure no fumes are present.
  On PWCs remove seats and compartments to let air in.
  Watch for leaks on all boats and have them fixed immediately!

## Slide 39: BACKFIRE FLAME ARRESTOR
Stops sparks entering the engine compartment.
Carbon build-up restrict gas flow and can glow.
Notes: Stops sparks entering the engine compartment. For more information check Chapter 13 “Engines for Sailboats”

## Slide 40: Fire Extinguishers

## Slide 41: Extinguisher Characteristics
Portable extinguishers are rated by “Size I or II” and “a number before the fuel identifier letter”, e.g., Size I, 2A:5B:C.
A fuel: number is equivalent to x1.25gal water,
2A = 2.5 gal.
B fuel: number is extinguished area in sq. feet, 5B = 5 sq ft (a square 2.2 x 2.2ft)
C fuel: no number. No power, no electrical fire.
(Quick Response Fire Supply, 17Jun2019-online)
Do NOT test an extinguisher by operating it.
UL number mean under optimal conditions:
Notes: Dry Chemical – uses fine spray of: sodium bicarbonate (NaHCO3, baking soda), potassium bicarbonate (KHCO3, nearly identical to baking soda), or monoammonium phosphate ((NH4)H2PO4) – most common.

## Slide 42
Pressure gauge or indicator
must be in “green”.
Handle locked firmly in place.
Discharge nozzle clean.
No visible signs of corrosion/damage.
Replace after 12 years from mfg. date.
Marine Fire Extinguisher

## Slide 43: Dry Chemical Extinguishers
Cylinders have pressure gauge
white - disposable
red - rechargeable
Filled with fine yellow powder (dry chemical); pressurized nitrogen as propellant.
Powder may consolidate,
check regularly.
Size I – 5B:C to 2A:10B:C
Size II – 20B:C
I
II
Notes: Dry Chemical – uses fine spray of: sodium bicarbonate (NaHCO3, baking soda), potassium bicarbonate (KHCO3, nearly identical to baking soda), or monoammonium phosphate ((NH4)H2PO4) – most common.

## Slide 44: No. Fire Extinguishers per Boat
2018: B-I & B-II designation changed to S-I & S-II.
Disposable FEs must be replaced after 12 years.
https://www.boatus.org/fire-extinguishers/ (06May2022)
Halon banded, Halotron or FE241 alternatives.
Boat length | No fixed system | Fixed system
< 26’ | One S-I | 0
26 to 40’ | Two S-I or One S-II | One S-I
40 to 65’ | Three S-I or One S-I and One S-II | Two S-I or One S-II
These are legal minimum numbers (more is better).
Notes: SO = in full, for UL: a 10-B:C extinguisher is effective on Class B and C fires, and has 2x the extinguishing capacity of a 5-B:C extinguisher.
Fixed System: uses inert gas to replace oxygen. Halon (banned since 1994). Halotron (EPA-approved), and other alternatives, 70% as effective as Halon.
USCG uses B-I and B-II because they are the most likely fuels to be found in boat fires.

## Slide 45: How to Use a Fire Extinguisher
P.A.S.S:
Pull
Aim
Squeeze
Sweep
Dry chemical: stand back 8’-12’ and always have your back to an escape route.
Notes: Aim at the BASE otherwise a blow-back.
Squeeze gently at first. Full blast likely to spread the fire.

## Slide 46
10 minutes to check your boat as the tide has come in.
Break
Notes: This is what happens when you anchor road is to short and the tide comes in.

## Slide 47: Boat Engine Cutoff Switch
Effective April 1, 2021
Recreational Boat Engine Cutoff Switch Requirements:
Congress Passes two laws:
Manufacturers to install engine cutoff switches on recreational vessels.
Recreational vessel operators requires to use the engine cutoff switch.
Designed to reduce potential of propellor injuries from runaway boats.
Notes: Over the last three years (2018-2020), Congress has passed two laws requiring, first, that manufacturers install engine cut-off switches on recreational vessels and, second, that recreational vessel operators use those engine cut-off switches. The laws that have placed these requirements on recreational vessel manufacturers and recreational vessel operators are found in United States Code (USC), as opposed to the Code of Federal Regulations (CFR) where these types of requirements are typically found. These are federal laws and not enforceable by state and local marine officers at this time. These new laws will improve safety for all recreational boaters by reducing the potential for propeller injuries to recreational vessel operators, other users of the nation’s waterways, and marine law enforcement officers responsible for responding to runaway boats.

## Slide 48: Boat Engine Cutoff Switch
Applies to recreational vessels under 26’, with engines capable of 115 pounds of thrust (approx. 3 HP) built after Jan 2021.
Act requires manufacturer, distributor or dealer of those vessels or motors to equip them with the ECOS.
If fitted, they must be
used when on plane.
Not necessary if helm
is in a ‘cabin’.

## Slide 49
USCG Boating Statistic for 2021
Accidents reported: 4,439. (Many are not.)
Injuries: 2,641. Definition: Situation where person requires medical attention.
Deaths: 658. (5.5 / 100,000 registered boats)
Fatal drowning: 488.
Person could swim: 439.
Not wearing PFD: 409.
No boating safety class taken: 468.
Good news, number of deaths down slightly.
Bad news, paddle craft number still rising.
Don’t be one of the 5.3 people in the 2023.

## Slide 50
Life Jackets (=LJs)
Why wear a LJ? – It’s an adult’s choice, but under 11 in ME (13 for USCG), must wear by Law.
Keeps you afloat, reduces the need for limb
motion – saves energy, buys you time.
Keeps you afloat through cold shock and
cold incapacitation; a “floater” easier to find.
LJs MUST have USCG approved label, be
in a serviceable condition, correct size and
adjusted for user; add user and boat names.
One Life Jacket (correctly sized) for each person aboard.

## Slide 51
Life Jackets
Most adults with lungs full have about 11lbs (50N) of buoyancy, mouth about water level.
Choose the “best” LJ for you and your type of boating.
Check LJs are: NOT ripped, worn, clips and zips broken, or air leaks in inflatables.
The old USCG labeling system is not understood by most boaters, so a new ‘Harmonized Standard’ system using icons was developed.

## Slide 52
Life jacket labelling – old and new
Notes: Use names and state they have intrinsic buoyancy (foam).
lbs now replaced by Newtons. International unit for buoyancy – don’t get into a discussion, emphasizes equivalents.
Use of Newtons allows same LJs to be sold in Canada, Mexico and world-wide.
Concentrate on 50, 70, 100 and 150; focus on middle 2.
Focus on the 3 names and PIW icon, Then on face-up icon.
Inflatables are special, no intrinsic buoyancy so not in intrinsic list and dealt with separately.

## Slide 53
PFD (old) Life jacket (new) labels
Notes: Information on old system not easy to see
Same information in new icons.
Explain “Not approved for” ions. First, International icon for “warning”. Last one white water sports.

## Slide 54
Offshore (old Type I)
International orange, reflective tape, light & whistle.
Provides best chance of survival, supports neck.
Bulky and restricts movement.
Usually considered commercial.
Buoyancy 22 lbs
Definition: Designed to turn most
unconscious wearers face up.
Notes: Both systems given but new is emphasized.

## Slide 55
Nearshore (old Type II)
Support for head
More comfortable than Type I, less bulky.
Definition: Designed to turn most unconscious wearers face up.
Buoyancy 15.5+ lbs

## Slide 56
Flotation Aid (old Type III )
Keeps wearer afloat (face-up or down)!
Most comfortable type.
Many designs are based on a particular sport, e.g., kayaking, fishing, water skiing, etc.
Definition: Calm inland waters, Not designed to turn you face up.
Buoyancy 15.5+ lbs
General type
Water skiing
Notes: Greater freedom of movement.
Not for heavy weather.
Greater freedom of arm movement

## Slide 57
Non-adults
Infant: 8 to 30lbs
Child: 30 to 50lbs
Youth: 50 to 90lbs
Make sure the youth has the correct rated LJ; wrong buoyance, dangerous.
LJ designs good for most individuals, but a few may turn them face down. Get another design; test new LJs before boating.
Ensure crotch strap is used!
CHILD COMFORT!
No child inflatable, MUST be 16>.

## Slide 58
TEST PROCEDURE

## Slide 59
Inflatables (Special Purpose – old type V)
NO inherent buoyancy! More comfortable.
Methods of Inflation:
  Manual inflation, pull on tab.
  Automatic inflation 2 mechanisms:
    Water dissolves a bobbin, inflates.
    Hydrostatic pressure release (initiated when more than 4” deep.)
  Back-up: inflate through mouth tube.

## Slide 60
Recreational Inflatables – 15.5 to 38lbs buoyancy:
Compact and comfortable to wear.
Head support, only has buoyancy when inflated. Uninflated or punctured NO buoyancy!
Special Purpose (Type V)
Inflatation automatic, will turn most unconscious wearers face up. 150N
(Type V & II)
Inflatation manual, unconscious person can’t pull toggle. 70N
(Type V & III)

## Slide 61
Level 70N
7.5lbs foam + 12.5lbs inflation manual = 20lbs total buoyancy.
LJs designed for particular sports
Hybrid: Enough foam to keep wearer’s body on water, manual inflation for full buoyancy.
Belt type: Manual inflation, 150N (35lbs) buoyancy, must pull over head. Bass Fishing etc.
Notes: More information on Life Jacket will be cover in Chapter 10 “Sailing Safety” (Chapter 8 “Boating Skills and Seamanship”)

## Slide 62
Inflatables Video

## Slide 63
LJs should have:
Attached whistle to PFD (USCG approved). Sound carries further than you can shout.
Signal light, 50 flashes/ min., continuous for 9hrs.

## Slide 64: Sound Producing Devices
Covered in detail later
A bell is only required for all vessels 20 meters (65’) and over.
Notes: Will be covered more in Chapter 6

## Slide 65
THROWABLE DEVICES
Must be USCG approved and on all boat 16’ >.
Ring buoys must be white or orange; reflective tape, name of boat.
Buoyant cushions. Choose red or orange. Blue and white not easy to see in water.
Attached life-lines always through ring. Good: person can be pulled to boat. Bad: line in the water and possible danger to propeller.

## Slide 66: Visual Distress Signals (Chap. 8)
USCG: Boats <16’, open sailboats <26’, manually propelled boats; do not need day signals but operating at night must have night signals.
USCG
State: VDS not required on Inland Waters, suggested.

## Slide 67: Boating Accident
Responsible for:
  Safety of crew
  Safety of boat
  Damage to others
Remember the 3C’s of Seamanship:
  Caution
  Courtesy
  Common sense
Reprinted with permission from Seaworthy: Essential Lessons From Boat U.S. 20 year case file of things Gone Wrong by Robert Adriance

## Slide 68: Boating Accident Reporting
Federal Requirements when:
  A death is involved, or person is missing.
  Loss of life-report within 48 hours, otherwise within 5 days.
  Injury requiring more than first aid.
  Property damage exceeds $2,000.
  Complete loss of boat.
Stop, inform USCG, assess situation, render aid if possible but do not endanger boat or crew.

## Slide 69: Boating Accident Reporting
Maine State Requirements when:
  Loss of life – report within 24 hours, otherwise within 5 days
  The operator must report the accident in writing within 72 hours if the damage to vessel or other property damage exceeds $2,000
Reports used for collecting statistical data
  Not made public
Notes: ME Accident Reports.
The operator of any vessel involved in a collision, accident, or other casualty has a duty to render aid to others that were involved or affected by the collision or accident if they can do so without serious damage to his or her own vessel, crew or passengers. The aid rendered should be that which may be practicable and necessary in order to save them from or minimize any danger caused by the incident.
The operator of any vessel involved must provide his or her name, address, and vessel registration to any person who was injured during the incident and to the owner of any property damaged by the incident.
The operator of any vessel involved in a collision, accident, or other casualty which results in death or personal injury that requires medical treatment beyond first aid, or damage to property in excess of five hundred dollars ($2,000) must file a full description of the incident with the Maine Wildlife Resources Authority on Maine Boating Accident Report Form.
An accident report in a case involving a loss of life must be submitted to the ME Environmental Police within forty-eight (48) hours of the incident.
An accident report in a case involving a reportable injury or property damage as described above must be submitted to the Department within five (5) days of the incident.
An accident report must be submitted in person or by mail to the ME Environmental Police Box 1325 Augusta ME.

## Slide 70: Alcohol and Drugs
Alcohol is a contributing factor in many boating accidents and deaths.
If you use alcohol or drugs your chances of surviving an accident are reduced.
Legal drugs can impair physical ability and judgement just as much as illegal one.

## Slide 71: MARINE SANITATION DEVICES (MSDs)
No requirement to install
Installed Heads:
  Must be Coast Guard certified
  type I, II, or III (A & B).
  Holding tanks use an
  approved pump out stations!
Illegal to have unapproved MSD
ALL Maine waters are no discharge zones even though approved MSD are installed.
‘Y’ valves secured, or head door locked.
Notes: MARINE SANITATION DEVICES
Motorboats with marine toilets are not allowed on public waters unless the toilet is equipped with a Type I, II or III marine sanitation device (MSD.) Type I and II MSDs chemically treat sewage. Type III MSDs are holding tanks for raw sewage.
Raw sewage shall not be discharged in any public waters. Type I and II MSDs must be sealed or locked while the vessel is on “no discharge” waters.

## Slide 72: International Marine Pollution Law
Notes: No trash, garbage or waste overboard in waters of USA. This or similarly worded decal is to be applied to boats 26 feet and longer as reminder to not pollute. Applies to all boaters.

## Slide 73: Oil/Fuel Spills
Report spills immediately. USCG at 1-800-424-8802
Placard displayed on vessels 26 feet and longer’
Notes: The discharge of oil and hazardous substances is strictly prohibited by the regulations issued under the Federal Water Pollution Control Act. This act requires all boats with propulsion machinery to have a capacity to retain oil mixtures onboard.
You are not allowed to discharge oil or hazardous substances.
You are not allowed to sump oil into the bilge of the boat without means for proper disposal.
You must discharge oil wastes to a reception facility.
On recreational boats a bailer or bucket is adequate.
You must immediately notify the U.S. Coast Guard if your boat discharges oil or hazardous substances in the water. Call toll free 1-800-424-8802. Report the discharge’s location, color, source, substances, size and time observed.
If your boat is 26’ or longer you must display a 5” x 8” placard made of durable material fixed in a conspicuous place in the machinery spaces, or at the bilge pump control station stating the following:

## Slide 74: Emergency Position-Indicating Radio Beacon (EPIRB) & PLBs
Not required on recreational vessels.
Are expensive but good to have.
Covered in more detail in later in the course.
Personal Locator Beacons (PLBs)

## Slide 75: Vessel Safety Checklist – required
Ventilation
Backfire Flame Arrester
Numbering
Life Jackets
Fire Extinguishers
Sound Producing Device
Navigation Lights
Visual Distress Signals

## Slide 76: Additional Equipment
Anchor and line
Spare parts and tool kit
Compass and charts
VHF-FM marine Radio
Docking lines
Fenders
First aid kit
Water for emergencies
Flashlight
Spare bulbs
Paddle
Dewatering devices
Boathook

## Slide 77: Vessel Safety Check
Asking for a Vessel Safety Check is a good way to have an extra set of eyes look at your boat.
Any Questions?